## Slide 1: FPGA 101 -Workshop
HACKADAY BELGRADE 26th MAY 2018
Miodrag Milanović

## Slide 2: Introduction
Engineer
Hardware and emulation enthusiast
Software developer since year 2000
Software architect at “Levi Nine” Serbia
Worked in C,C++,C# and Java
Working on MAME emulation project since 2006
Gave few talks related to FPGA targeting software developers.

## Slide 3: THANKS
Jan Dolinaj – for helping making these boards
David Shah – for great help in designing boards
Grant Jennings and Lattice – for Upduino 2 board and support
OSH Park and Drew Fustini – for sponsoring PCB production
IcoTC and Clifford Wolf – for excellent tools and logistic support for project
Jesús Arroyo Torrens and Juan González for APIO and IceStudio
Risc-V and MicroPython community
Hackaday for creating this great event

## Slide 4: WHAT WE ARE GOING TO LEARN ?
What is FPGA and how it works
How to use visual design tools to create hardware solutions
Verilog basics
How to create audio and video
Create CPU
Use existing Risc-V CPU core and run C programs on it
Run MicroPython on FPGA and program directly on it
And much more …

## Slide 5: Approach

## Slide 9: LET’s START

## Slide 10: Logic LEVELS
1
0
X
Z

## Slide 11: Boolean operations
AND
OR
XOR
NOT
NAND
NOR
XNOR
INPUT |  | OUTPUT |  |  |  |  | 
A | B | A AND B | A NAND B | A OR B | A NOR B | A NOR B | A XNOR B
0 | 0 | 0 | 1 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 1 | 0 | 1 | 0
1 | 0 | 0 | 1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 1 | 0 | 0 | 1

## Slide 12: D Flip-Flop
CLK | D | R | S | Q | !Q
rising edge | 0 | 0 | 0 | 0 | 1
rising edge | 1 | 0 | 0 | 1 | 0
falling edge | x | 0 | 0 | Q | !Q
x | x | 1 | 0 | 0 | 1
x | x | 0 | 1 | 1 | 0
x | x | 1 | 1 | 1 | 1
D
CLK
Q
!Q
CLK
Rising edge
Falling edge

## Slide 13: What is FPGA ?
Field-programmable gate array
Logic block – LUT + D Flip-Flop + full adder
I/O block – one per each pin
Interconnections, clock tree
Hard block – Block RAM, multipliers, DSP, CPU,…
Vendors: Xilinx, Intel/Altera, Lattice, Microsemi …

## Slide 14: Logic block
LUT
Full
Adder
MUX
MUX
MUX
D
Flip-Flop
Clock
Carry in
Carry out
Input
Output

## Slide 15: How do we program FPGA ?
HDL - Hardware description language
VHDL and Verilog
Analysis: parsing and validation of HDL
Synthesis: HDL -> netlist
Place-and-route: netlist -> specific FPGA technology
Assembler: specific FPGA technology -> bitstream
Programming: deploying bitstream on device (serial flash memory or directly)
Timing analysis
Simulation

## Slide 16: Open source tools
Yosys - Verilog synthesis tool by Clifford Wolf
Arachne PnR - Place and route tool by Cotton Seed
Project IceStorm – Assembler, time analysis and FPGA programming tool
by Clifford Wolf and Mathias Lasser
APIO – micro-ecosystem for open FPGAs by Jesús Arroyo Torrens and Juan González (Obijuan)
Icestudio - graphic editor for open FPGAs by Jesús Arroyo Torrens
Lattice iCE40 FPGA only

## Slide 17: And more…
Icarus Verilog by Stephen Williams
Verilator by Wilson Snyder with Duane Galbi and Paul Wasson
FuseSoC - package manager and a set of build tools for FPGA/ASIC development by Olof Kindgren

## Slide 18: LET’s SETUP

## Slide 19: Install DRIVERS
apio drivers --ftdi-enable
apio system –lsftdi
  Number of FTDI devices found: 1
  Checking device: 0
  Manufacturer: FTDI, Description: Single RS232-HS
apio system –lsserial
  Number of Serial devices found: 1
  COM3
  Description: USB-SERIAL CH340 (COM3)
  Hardware info: USB VID:PID=1A86:7523 SER=5 LOCATION=1-13

## Slide 20: Windows update driver

## Slide 21: Icestudio

## Slide 31: BASICS

## Slide 32: CREATE APIO PROJECT
[env]
board = fpga101
apio init --board fpga101
Creating apio.ini file ...
File 'apio.ini' has been successfully created!

## Slide 33: PCF FILE
# 12 MHz clock
set_io -nowarn CLK 35 # input
# LCD connector
set_io -nowarn LCD_CLK 18 # output
set_io -nowarn LCD_DEN 19 # output
set_io -nowarn LCD_VS 11 # output
set_io -nowarn LCD_HS 9 # output
set_io -nowarn LCD_RST 2 # output
set_io -nowarn LCD_D7 6 # output
set_io -nowarn LCD_D6 44 # output
set_io -nowarn LCD_D5 4 # output
set_io -nowarn LCD_D4 3 # output
set_io -nowarn LCD_D3 48 # output
set_io -nowarn LCD_D2 45 # output
set_io -nowarn LCD_D1 47 # output
set_io -nowarn LCD_D0 46 # output
set_io -nowarn LCD_PWM 13 # output
# Buttons
set_io -nowarn B0 23 # input
set_io -nowarn B1 25 # input
set_io -nowarn B2 26 # input
set_io -nowarn B3 27 # input
set_io -nowarn B4 21 # input
set_io -nowarn B5 12 # input
# Audio jack
set_io -nowarn AUDIO 37 # output
# PMOD connector
set_io -nowarn PMOD0 32
set_io -nowarn PMOD1 31
set_io -nowarn PMOD2 34
set_io -nowarn PMOD3 43
set_io -nowarn PMOD4 36
set_io -nowarn PMOD5 42
set_io -nowarn PMOD6 38
set_io -nowarn PMOD7 28
# RGB LED Driver
set_io -nowarn LED_G 39 # output
set_io -nowarn LED_B 40 # output
set_io -nowarn LED_R 41 # output

## Slide 34: LED.V (VERILOG FILE)
module led (
output LED_B
);
assign LED_B = 1'b0;
endmodule

## Slide 35: LED - COUNTER

## Slide 36: COUNTER
module rgb (
input CLK,
output LED_R,
output LED_G,
output LED_B,
output LCD_PWM
);
assign LCD_PWM = 1'b0;
reg [32:0] clk_cnt;
initial
begin
clk_cnt = 0;
end
always @(posedge CLK)
begin
clk_cnt <= clk_cnt + 1;
end
assign LED_R = !clk_cnt[2];
assign LED_G = !clk_cnt[3];
assign LED_B = !clk_cnt[4];
endmodule

## Slide 37: TEST BENCH
`timescale 1ns/1ps
module rgb_tb();
reg clk = 0;
wire led_r;
wire led_g;
wire led_b;
wire led_pwm;
rgb leds(.CLK(clk),.LED_R(led_r),.LED_G(led_g),
.LED_B(led_b),.LCD_PWM(led_pwm));
always
#(5) clk <= !clk;
initial
begin
$dumpfile("rgb_tb.vcd");
$dumpvars(0,rgb_tb);
#1000
$finish;
end
endmodule

## Slide 38: APIO TOOLS
apio verify
iverilog -o hardware.out -D VCD_OUTPUT= "C:\msys64\opt\homedir\.apio\packages\toolchain-iverilog\vlib\cells_sim.v" rgb.v
========================= [SUCCESS] Took 0.30 seconds============================
apio lint
verilator --lint-only -IC:\msys64\opt\homedir\.apio\packages\toolchain-verilator\share rgb.v
========================= [SUCCESS] Took 0.21 seconds============================
apio sim
iverilog -o rgb_tb.out -D VCD_OUTPUT=rgb_tb "C:\msys64\opt\homedir\.apio\packages\toolchain-iverilog\vlib\cells_sim.v" rgb.v rgb_tb.v
vvp rgb_tb.out
VCD info: dumpfile rgb_tb.vcd opened for output.
gtkwave rgb_tb.vcd rgb_tb.gtkw

## Slide 40: BUTTONS

## Slide 41: DIRECT CONNECTION
module button_rgb (
input CLK,
output LED_R,
output LED_G,
output LED_B,
output LCD_PWM,
input B0,
input B1,
input B2
);
assign LCD_PWM = 1'b0;
assign LED_R = !B0;
assign LED_G = !B1;
assign LED_B = !B2;
endmodule

## Slide 42: BUTTON AS TRIGGER
module button_cnt (
input CLK,
output LED_R,
output LED_G,
output LED_B,
output LCD_PWM,
input B0
);
reg [2:0] cnt = 0;
always @(posedge B0)
begin
cnt <= cnt + 1;
end
assign LCD_PWM = 1'b0;
assign LED_R = !cnt[0];
assign LED_G = !cnt[1];
assign LED_B = !cnt[2];
endmodule

## Slide 43: BUTTON DEBOUNCER
module button_rgb (
input CLK, output LED_R, output LED_G, output LED_B,
output LCD_PWM, input B0
);
reg [24:0] clk_cnt;
reg [2:0] cnt = 0;
reg prev = 0;
always @(posedge CLK)
begin
clk_cnt <= clk_cnt + 1;
end
always @(posedge clk_cnt[20])
begin
prev <= B0;
if (prev == 1'b0 && B0 == 1'b1)
cnt <= cnt + 1;
end
assign LCD_PWM = 1'b0;
assign LED_R = !cnt[0];
assign LED_G = !cnt[1];
assign LED_B = !cnt[2];
endmodule

## Slide 44: Exercise
Map different buttons to different RGB colors

## Slide 45: AUDIO

## Slide 46: THEORY
Digital – Analog Converter
PWM
We will change frequency of change, but keep 50% duty cycle

## Slide 47: PLAY SOUNDS
module audio(
input CLK,
output LCD_PWM,
input B0,
input B1,
input B2,
input B3,
input B4,
input B5,
output reg AUDIO);
parameter TONE_A4 = 12000000/440/2;
parameter TONE_B4 = 12000000/494/2;
parameter TONE_C5 = 12000000/523/2;
parameter TONE_D5 = 12000000/587/2;
parameter TONE_E5 = 12000000/659/2;
parameter TONE_F5 = 12000000/698/2;
parameter TONE_G5 = 12000000/783/2;
reg [14:0] counter;
always @(posedge CLK)
if(counter==0)
counter <= (
B0 ? TONE_A4-1 :
B1 ? TONE_B4-1 :
B2 ? TONE_C5-1 :
B3 ? TONE_D5-1 :
B4 ? TONE_E5-1 :
B5 ? TONE_F5-1 : 0);
else
counter <= counter-1;
always @(posedge CLK)
if(counter==0)
AUDIO <= ~AUDIO;
assign LCD_PWM = 1'b0;
endmodule

## Slide 48: Exercise
Make police car siren sound
Play full octave round and round

## Slide 49: VIDEO

## Slide 50: Theory
Vertical front porch
Vertical back porch
Vertical sync
Horizontal front
porch
Horizontal
back
porch
Horizontal sync
Visible area

## Slide 51: Clock generator
/* ------------------------
Clock generator
------------------------*/
wire clkhf;
wire locked;
wire pixclk;
(* ROUTE_THROUGH_FABRIC=1 *)
SB_HFOSC #(.CLKHF_DIV("0b01")) hfosc_i (
.CLKHFEN(1'b1),
.CLKHFPU(1'b1),
.CLKHF(clkhf)
);
pll pll_i(.clock_in(clkhf), .clock_out(pixclk), .locked(locked))

## Slide 52: PLL
/*
* Given input frequency: 24.000 MHz
* Requested output frequency: 19.200 MHz
* Achieved output frequency: 19.125 MHz
*/
module pll(
input clock_in,
output clock_out,
output locked
);
SB_PLL40_CORE #(
.FEEDBACK_PATH("SIMPLE"),
.DIVR(4'b0001), // DIVR = 1
.DIVF(7'b0110010), // DIVF = 50
.DIVQ(3'b101), // DIVQ = 5
.FILTER_RANGE(3'b001) // FILTER_RANGE = 1
) uut (
.LOCK(locked),
.RESETB(1'b1),
.BYPASS(1'b0),
.REFERENCECLK(clock_in),
.PLLOUTGLOBAL(clock_out)
);
endmodule

## Slide 53: Video generator module
module video (
input clk, //19.2MHz pixel clock in
input resetn,
output reg [7:0] lcd_dat,
output reg lcd_hsync,
output reg lcd_vsync,
output reg lcd_den,
output reg [9:0] h_pos,
output reg [9:0] v_pos,
input [23:0] rgb_data
);

## Slide 54: ONE COLOR SCREEN
Exercise:
  Try different colors
  Try to change color depending of button 0
assign rgb_data = 24'hff0000;

## Slide 55: CHECKERS
assign rgb_data = (h_pos < 320) ?
h_pos[4] ^ v_pos[4] ? 24'h000000 : 24'hffffff :
24'h000000;

## Slide 56: STRIPES
assign rgb_data = (h_pos < 64) ? {h_pos[5:0], 18'd0} :
(h_pos < 128) ? {8'd0, h_pos[5:0], 10'd0} :
(h_pos < 192) ? {16'd0, h_pos[5:0], 2'd0} :
(h_pos < 256) ? {h_pos[5:0], 2'd0, h_pos[5:0], 2'd0, h_pos[5:0], 2'd0} :
(h_pos < 320) ? {h_pos[5:0], 2'd0, 8'd0, h_pos[5:0], 2'd0} :
24'd0;

## Slide 57: Key TEST
assign rgb_data =
(h_pos > 50 && h_pos < 100 && v_pos > 100 && v_pos < 150 && B0) ? 24'hffffff :
(h_pos > 100 && h_pos < 150 && v_pos > 50 && v_pos < 100 && B1) ? 24'hffffff :
(h_pos > 150 && h_pos < 200 && v_pos > 100 && v_pos < 150 && B2) ? 24'hffffff :
(h_pos > 100 && h_pos < 150 && v_pos > 150 && v_pos < 200 && B3) ? 24'hffffff :
(h_pos > 250 && h_pos < 300 && v_pos > 50 && v_pos < 100 && B5) ? 24'hff6633 :
(h_pos > 250 && h_pos < 300 && v_pos > 150 && v_pos < 200 && B4) ? 24'hff6633 :
24'h000000;

## Slide 58: Exercise
Update key-test example according to your board layout
Try generating flag image
Experiment with idea of your own 

## Slide 59: STATE MACHINES

## Slide 60: Simple state machine
reg [32:0] clk_cnt;
reg [1:0] state = 2'b00;
initial
begin
rgb_data <= 24'h0000ff;
end
always @(posedge pixclk)
begin
clk_cnt <= clk_cnt + 1;
case(state)
2'b00 : begin
    if (clk_cnt > 32'h02ffffff)
    begin
    rgb_data <= 24'hffffff;
    clk_cnt <= 32'd0;
    state <= 2'b01;
    end
end
2'b01 : begin

## Slide 61: Exercise
Add more states
Make buttons change state

## Slide 62: MEMORY

## Slide 63: SYNCED MEMORY
module font_rom(
input clk,
input [11:0] addr,
output [7:0] data_out
);
reg [7:0] store[0:4095];
initial
begin
$readmemh("font_vga.mem", store);
end
always @(posedge clk)
data_out <= store[addr];
endmodule

## Slide 64: Exercise
Change font/background color in example
Use your of custom text displayed
Try making text to be double width or double height when displayed

## Slide 65: SPRITES

## Slide 66: 4 bit wide indexed memory
module sprite_rom(
input clk,
input [11:0] addr,
output [23:0] data_out
);
wire [23:0] palette[0:15];
assign palette[0] = 24'h000000;
assign palette[1] = 24'h180002;
assign palette[2] = 24'h240001;
assign palette[3] = 24'h390100;
assign palette[4] = 24'h530000;
assign palette[5] = 24'h710000;
assign palette[6] = 24'h8a0000;
assign palette[7] = 24'ha20000;
assign palette[8] = 24'hba0000;
assign palette[9] = 24'hdd0002;
assign palette[10] = 24'hff0000;
assign palette[11] = 24'hff3031;
assign palette[12] = 24'hff5f62;
assign palette[13] = 24'hff8d8b;
assign palette[14] = 24'hffcccb;
assign palette[15] = 24'hffffff;
reg [3:0] store[0:4095];
initial
begin
$readmemh("sprite.mem", store);
end
always @(posedge clk)
data_out <= palette[store[addr]];
endmodule

## Slide 67: Display SPRITE
wire [23:0] sprite_rgb;
reg [10:0] pos_x = 100;
reg [10:0] pos_y = 100;
wire [10:0] sprite_x;
wire [10:0] sprite_y;
assign sprite_x = h_pos - pos_x;
assign sprite_y = v_pos - pos_y;
sprite_rom sprite(
.clk(pixclk),
.addr({ sprite_y[5:0], sprite_x[5:0] }),
.data_out(sprite_rgb)
);
assign rgb_data = (h_pos > pos_x && h_pos < pos_x + 64
&& v_pos > pos_y && v_pos < pos_y + 64) ? sprite_rgb :
24'hffffff;

## Slide 68: MOVE SPRITE
localparam SCREEN_WIDTH = 320;
localparam SCREEN_HEIGHT = 240;
reg [10:0] sprite_vel_x = 1;
reg [10:0] sprite_vel_y = -1; always @(posedge cnt[17])
begin
if (pos_x == 0)
begin
sprite_vel_x <= 1;
end
if (pos_x + 64 == SCREEN_WIDTH)
begin
sprite_vel_x <= -1;
end
if (pos_y == 0)
begin
sprite_vel_y <= 1;
end
if (pos_y + 64 == SCREEN_HEIGHT)
begin
sprite_vel_y <= -1;
end pos_x <= pos_x + sprite_vel_x;
pos_y <= pos_y + sprite_vel_y;
end

## Slide 69: Exercise
Change speed of moving in example
Make sprite react on commands

## Slide 70: PONG

## Slide 71: Display pads and net
localparam SCREEN_WIDTH = 320;
localparam SCREEN_HEIGHT = 240;
localparam PADDLE_SIZE = 60;
localparam PADDLE_WIDTH = 10;
localparam NET_WIDTH = 2;
reg [8:0] paddle1_y = (SCREEN_HEIGHT-PADDLE_SIZE)/2;
reg [8:0] paddle2_y = (SCREEN_HEIGHT-PADDLE_SIZE)/2;
assign rgb_data =
(h_pos > 0 && h_pos < PADDLE_WIDTH && v_pos > paddle1_y && v_pos < paddle1_y + PADDLE_SIZE) ? 24'hffffff :
(h_pos > (SCREEN_WIDTH-PADDLE_WIDTH) && h_pos < SCREEN_WIDTH && v_pos > paddle2_y && v_pos < paddle2_y + PADDLE_SIZE) ? 24'hffffff :
(h_pos > (SCREEN_WIDTH/2) - NET_WIDTH && h_pos < (SCREEN_WIDTH/2) + NET_WIDTH && v_pos[4]==0) ? 24'hffffff :
24'h000000;

## Slide 72: Moving PADS
reg [31:0] cnt;
always @(posedge clk)
begin
cnt <= cnt + 1;
end
always @(posedge cnt[16])
begin
if (B1==1'b1)
paddle1_y <= (paddle1_y > 0) ? paddle1_y - 1 : paddle1_y;
if (B3==1'b1)
paddle1_y <= (paddle1_y < (SCREEN_HEIGHT-PADDLE_SIZE)) ? paddle1_y +1 : paddle1_y;
if (B5==1'b1)
paddle2_y <= (paddle2_y > 0) ? paddle2_y - 1 : paddle2_y;
if (B4==1'b1)
paddle2_y <= (paddle2_y < (SCREEN_HEIGHT-PADDLE_SIZE)) ? paddle2_y +1 : paddle2_y;
end

## Slide 73: Exercise
Change color of elements on screen
Add obstacles on field
Try expanding “The Wall” game code

## Slide 74: CPU

## Slide 75: Instruction SET (1/2)
IR |  |  | 2nd | Instruction | Info
0000 | dst | src |  | MOV dst, src | 
0001 | 00 | reg |  | ADD reg | r0 = r0 + reg
0001 | 01 | reg |  | SUB reg | r0 = r0 - reg
0001 | 10 | reg |  | ADC reg | r0 = r0 + reg + C
0001 | 11 | reg |  | SBC reg | r0 = r0 - reg - C
0010 | 00 | reg |  | AND reg | r0 = r0 and reg
0010 | 01 | reg |  | OR reg | r0 = r0 or reg
0010 | 10 | reg |  | NOT reg | r0 = not reg
0010 | 11 | reg |  | XOR reg | r0 = r0 xor reg
0011 | 00 | reg |  | INC reg | reg = reg + 1
0011 | 01 | reg |  | DEC reg | reg = reg - 1
0011 | 10 | reg |  | CMP reg | flags of r0 - reg
0011 | 11 | reg |  | TST reg | flags of r0 and reg
0100 | 00 | 00 |  | SHL | 
0100 | 00 | 01 |  | SHR | 
0100 | 00 | 10 |  | SAL | 
0100 | 00 | 11 |  | SAR | 
0100 | 01 | 00 |  | ROL | 
0100 | 01 | 01 |  | ROR | 
0100 | 01 | 10 |  | RCL | rotate with carry
0100 | 01 | 11 |  | RCR | rotate with carry
0100 | 10 | reg |  | PUSH reg | 
0100 | 11 | reg |  | POP reg | 
0101 | dst | src |  | LOAD dst, [src] | 
0110 | dst | src |  | STORE [dst], src | 
0111 | 00 | reg |  | MOV CS, reg | 
0111 | 01 | reg |  | MOV DS, reg | 
0111 | 10 | 00 |  | PUSH CS | 
0111 | 10 | 01 |  | PUSH DS | 
0111 | 10 | 10 |  | ??? | 
0111 | 10 | 11 |  | ??? | 
0111 | 11 | 00 |  | ??? | 
0111 | 11 | 01 |  | ??? | 
0111 | 11 | 10 |  | RET | 
0111 | 11 | 11 |  | HLT | 

## Slide 76: Instruction SET (2/2)
1000 | 00 | 00 | val | JMP val | (unconditionally jump)
1000 | 00 | 01 | val | JC val | (carry=1 jump)
1000 | 00 | 10 | val | JNC val | (carry=0 jump)
1000 | 00 | 11 | val | JM val | (sign=1 jump)
1000 | 01 | 00 | val | JP val | (sign=0 jump)
1000 | 01 | 01 | val | JZ val | (zero=1 jump)
1000 | 01 | 10 | val | JNZ val | (zero=0 jump)
1000 | 01 | 11 | val | ??? | 
1000 | 10 | 00 | val | JR val | (unconditionally jump)
1000 | 10 | 01 | val | JRC val | (carry=1 jump)
1000 | 10 | 10 | val | JRNC val | (carry=0 jump)
1000 | 10 | 11 | val | JRM val | (sign=1 jump)
1000 | 11 | 00 | val | JRP val | (sign=0 jump)
1000 | 11 | 01 | val | JRZ val | (zero=1 jump)
1000 | 11 | 10 | val | JRNZ val | (zero=0 jump)
1000 | 11 | 11 | val | ??? | 
1001 | high |  | low | JUMP addr | 
1010 | high |  | low | CALL addr | 
1011 | high |  | low | MOV SP,addr | 
1100 | xx | reg | val | IN reg,[val] | 
1101 | xx | reg | val | OUT [val],reg | 
1110 | xx | 00 | val | MOV CS,val | 
1110 | xx | 01 | val | MOV DS,val | 
1110 | xx | 10 | val | ??? | 
1110 | xx | 11 | val | ??? | 
1111 | 00 | reg | val | MOV reg, val | 
1111 | 01 | reg | val | LOAD reg, [val] | 
1111 | 10 | reg | val | STORE [val], reg | 
1111 | 11 | xx |  | ??? | 

## Slide 77: ALU
ALU_OP_ADD :
tmp = A + B;
ALU_OP_SUB :
tmp = A - B;
ALU_OP_ADC :
tmp = A + B + { 7'b0000000, CF };
ALU_OP_SBC :
tmp = A - B - { 7'b0000000, CF };
ALU_OP_AND :
tmp = {1'b0, A & B };
ALU_OP_OR :
tmp = {1'b0, A | B };
ALU_OP_NOT :
tmp = {1'b0, ~B };
ALU_OP_XOR :
tmp = {1'b0, A ^ B};
ALU_OP_SHL :
tmp = { A[7], A[6:0], 1'b0};
ALU_OP_SHR :
tmp = { A[0], 1'b0, A[7:1]};
ALU_OP_SAL :
// Same as SHL
tmp = { A[7], A[6:0], 1'b0};
ALU_OP_SAR :
tmp = { A[0], A[7], A[7:1]};
ALU_OP_ROL :
tmp = { A[7], A[6:0], A[7]};
ALU_OP_ROR :
tmp = { A[0], A[0], A[7:1]};
ALU_OP_RCL :
tmp = { A[7], A[6:0], CF};
ALU_OP_RCR :
tmp = { A[0], CF, A[7:1]};

## Slide 78: Exercise
Change executed binary
Add new instruction of your choice

## Slide 79: COMPUTER

## Slide 80: MAPPING MEMORY READS
casex ({boot,sysctl[6],addr[15:8]})
// Turn-key BOOT
{2'b10,8'bxxxxxxxx}: begin idata = boot_out; rd_boot = rd; end // any address
// MEM MAP
{2'b00,8'b000xxxxx}: begin idata = rammain_out; rd_rammain = rd; end // 0x0000-0x1fff
{2'b00,8'b11111011}: begin idata = ram_out; rd_ram = rd; end // 0xfb00-0xfbff
{2'b00,8'b11111101}: begin idata = rom_out; rd_rom = rd; end // 0xfd00-0xfdff
// I/O MAP - addr[15:8] == addr[7:0] for this section
{2'b01,8'b000x000x}: begin idata = sio_out; rd_sio = rd; end // 0x00-0x01 0x10-0x11
endcase

## Slide 81: MAPPING MEMORY WRITES
casex ({sysctl[4],addr[15:8]})
// MEM MAP
{1'b0,8'b000xxxxx}: wr_rammain = ~wr_n; // 0x0000-0x1fff
{1'b0,8'b11111011}: wr_ram = ~wr_n; // 0xfb00-0xfbff
// 0xfd00-0xfdff read-only
// I/O MAP - addr[15:8] == addr[7:0] for this section
{1'b1,8'b000x000x}: wr_sio = ~wr_n; // 0x00-0x01 0x10-0x11
endcase

## Slide 82: MAPPING DEVICES
I8080 cpu (.clk(clk),.ce(ce),.reset(reset),.intr(intr),.idata(idata),.addr(addr),.sync(sync),.rd(rd),.wr_n(wr_n),.inta_n(inta_n),.odata(odata),.inte_o(inte_o));
jmp_boot boot_ff(.clk(clk),.reset(reset),.rd(rd_boot),.data_out(boot_out),.valid(boot));
rom_memory #(.ADDR_WIDTH(8),.FILENAME("turnmon.bin.mem"))
rom(.clk(clk),.addr(addr[7:0]),.rd(rd_rom),.data_out(rom_out));
ram_memory #(.ADDR_WIDTH(8)) stack(.clk(clk),.addr(addr[7:0]),.data_in(odata),.rd(rd_ram),.we(wr_ram),.data_out(ram_out));
ram_memory #(.ADDR_WIDTH(13),.FILENAME("basic4k32.bin.mem"))
mainmem(.clk(clk),.addr(addr[12:0]),.data_in(odata),.rd(rd_rammain),.we(wr_rammain),.data_out(rammain_out));
mc6850
sio(.clk(clk),.reset(reset),.addr(addr[0]),.data_in(odata),.rd(rd_sio),.we(wr_sio),.data_out(sio_out),.ce(ce),.rx(rx),.tx(tx));

## Slide 83: Exercise
Write your first Altair code in BASIC
Display text on LCD

## Slide 84: RISC-V

## Slide 85: Memory mapped I/O
#define reg_uart_clkdiv (*(volatile uint32_t*)0x02000004)
#define reg_uart_data (*(volatile uint32_t*)0x02000008)
#define reg_io ((volatile uint32_t*)0x03000000)
#define reg_text ((volatile uint32_t*)0x04000000)
#define reg_attr ((volatile uint32_t*)0x05000000)
#define reg_tone ((volatile uint32_t*)0x06000000)

## Slide 86: Send data over UART
void putchar(char c)
{
if (c == '\n')
putchar('\r');
if (c != '\r')
lcd_putch(c);
reg_uart_data = c;
}
void print(const char *p)
{
while (*p)
putchar(*(p++));
}

## Slide 87: Exercise
Display your own text by programming in C
Make terminal emulation in C
Write a small Q&A game

## Slide 88: MICROPYTHON

## Slide 89: Classic Python CODING
def fib(n):
a, b = 0, 1
while a < n:
print(a, end=' ‘)
a, b = b, a+b
print()
fib(1000)

## Slide 90: AcCessing LEDS
import pyb
def blinky():
for i in range(30):
pyb.LED(i % 3 + 1).on()
pyb.delay(100)
pyb.LED(i % 3 + 1).off()

## Slide 91: Accessing Buttons
import pyb
but0 = pyb.Switch(1)
but1 = pyb.Switch(2)
but0()

## Slide 92: Let’s PLAY SOUND
import pyb
pyb.tone(440, 100)
pyb.delay(100)
pyb.tone(440, 100)

## Slide 93: Display on LCD
import pyb
lcd = pyb.LCD()
lcd.clear()
lcd.move(5,5)
lcd.write("Test")
lcd.move(10,10)
lcd.write("Test")

## Slide 94: Exercise
Show me your Python skills 

## Slide 95: DeMOSTRATION

## Slide 96: Mikroelektronika
Click boards with FPGA
Order any Click board with provided 20% discount code (valid one month from now)